## Slide 1: Introduction to the FreeCAD GDML Workbench Keith Sloan & Munther Hindi 15th Geant4 Space Users Workshop Pasadena, December 2023
Notes: Thank you for organising this conference with its very laudable aim of developing much needed engineering skills capacity, enhanced safety standards, and infrastructure that will remain safe and fit for purpose. I think FreeCAD Engineering related workbenches also have a lot of potential to enable sustainable development. I hope and am sure the conference will be a great success and kick start a great future for FreeCAD in such an environment.

## Slide 2: GDML
GDML: Geometry Description Markup Language.
A specialized XML-based language designed for describing the geometries of detectors for physics experiments.
Integrated into Geant4 since release 9.2
Need to set GEANT4_USE_GDML = 1 when compiling
GDML Workbench: A tool for importing GDML files into (Free)CAD geometries and exporting FreeCAD geometries to GDML
<number>

## Slide 3: Abbreviated GDML file structure
<number>
Notes: GDML geometry
Define SectionConstants, Positions, Rotations Materials ( Elements ), Standard set of Geant4 materials (NIST)
Solids - Constructed Solid Geometries
Volumes - One Solid, One Material, Optional number of Physical Volumes
Physvols - Refer to Volumes, Position, Rotation, CopyNumber
Assembly - A group of Volumes

## Slide 4: FreeCAD – an Open Source CAD Application freecad.org
<number>

## Slide 5
Some Features(from the FreeCAD web site):
<number>

## Slide 6
GDML Workbench
GDML Workbench adds import/export of gdml files
FreeCAD features, continued
<number>

## Slide 7
FreeCAD features, continued
Sketch parameters can have numeric values (with units) or come from a FreeCAD supported spreadsheet. As usual, cells can have aliases and reference other cells.
Sketches can be converted to 3D solids by (a) extruding them (b) revolving them, (c) sweeping them along paths.
<number>

## Slide 8
Functionality of FreeCAD accessed through Workbenches:
Workbench: a set of tools + GUI grouped for a certain task.
Base Workbenches: installed with FreeCAD and
maintained by them
External Workbenches: Developed by the community and maintained outside FreeCAD
GDML: An external Workbench
<number>

## Slide 9
External Workbenches Installed Via Tools→Addon Manager
<number>

## Slide 10
FreeCAD
gdml file
GDML
Workbench
export
Geant4 application
read
Geant4 application
gdml file
GDML
Workbench
open or import
FreeCAD
write
In this presentation we concentrate on going from FreeCAD to gdml/Geant4:
But one can also go from a Geant4 geometry to FreeCAD (see example G01):
<number>

## Slide 11
Launch FreeCAD
Select GDML Workbench
Creating a gdml file from scratch
<number>

## Slide 12
Create New document
Creating a gdml file from scratch, continued
<number>

## Slide 13
<number>

## Slide 14
Pre-populated with an empty World Box
<number>

## Slide 15
Pre-populated with an empty World Box
Add GDML solid(s)
<number>

## Slide 16
<number>

## Slide 17
Default properties can be edited
<number>

## Slide 18
Default properties can be edited
This tree element in the
document exports to:
a) a <solid
b) a <volume
c) a <physvol
<number>

## Slide 19
Materials can be added in two ways:
1) From drop list in ‘material’ property
<number>

## Slide 20
Materials can be added in two ways:
2) Using ‘set material’ icon.
Allows incremental search
Allows adding material property to non-GDML solids.
<number>

## Slide 21
When a new document is created, a file supplied with the GDML Workbench (Geant4Materials.xml) is loaded. This file contains the Geant4 and NIST list of materials. The materials are displayed as a group with subgroups in the FreeCAD document.
At present new materials cannot be defined from within the GDML Workbench
New materials can be added directly to the supplied Geant4Materials.xml file, or read by opening or importing a user supplied gdml file.
Opening a gdml file creates a new document; importing it adds its contents to the currently open document
Materials
<number>

## Slide 22
Can add booleans (Cuts, Intersections, Unions) of inserted solids: select two solids then select the operation using the icons above.
<number>

## Slide 23
Export the document to gdml:
1) Select the worldVOL
<number>

## Slide 24
2) File → Export...
<number>

## Slide 25
3) Export as GDML
Export gdml - Single file with gdml definitions
Export GDML - directory with gdml sections as includes
<number>

## Slide 26
Can view the exported file using the load_gdml application provided with Geant4 in
examples/persistency/gdml/G01
We export the FreeCAD color of solids by adding an <auxiliary auxtype=”Color”> tag to each of the <volumes> in the gdml file.
We have a modified version of load_gdml, load_gdml_color that processes that auxiliary tag. We can add the modified file to the github if there is interest.
<number>

## Slide 27
Adding non-GDML solids to the GDML document
1. Extrusions
a) Click on the new sketch icon in the
GDML Workbench
b) create a closed sketch
c) close the sketch
<number>

## Slide 28
d) Select the sketch and extrude it to the desired height
<number>

## Slide 29
d) Select the sketch and extrude it to the desired height
e) Add a Part to the worldVOL tree
<number>

## Slide 30
d) Select the sketch and extrude it to the desired height
e) Add a Part to the worldVOL tree
f) Drag the Extrusion under the added Part
<number>

## Slide 31
Adding non-GDML solids to the GDML document
1. Extrusions
To the extent possible, extrusions are exported as booleans of GDML solids (Circles→Tubes, Polygons→ Xtru, Ellipses → ElTube, …). We believe this produces faster Geant4 simulations than conversion to a Tessellation:
With 106 geantinos:
extrusions: 7.25 s
tesselation: 17.35 s
(Factor of 2.4 faster with booleans)
With 106 2 MeV gamma rays:
extrusion: 17.35 s
tessellation: 146 s
(Factor of 8.4 faster with booleans)
Exported as booleans of Solids
Exported as tessellations
<number>

## Slide 32
Adding non-GDML solids to the GDML document
2. Revolve
View of exported gdml file containing a Revolved sketch, using load_gdml_color
Surfaces of revolution added by
creating curve(s) in Sketcher,
and then using the revolve command
Revolves are exported as gdml genericPolycone’s
<number>

## Slide 33
Adding non-GDML solids to the GDML document
3. Arrays
a. Orthogonal Arrays
Orthogonal arrays are added by selecting the object and executing the orthogonal array command
Note: Arrays of solids are exported as a single multiunion solid and will all have the same material
View of exported gdml file containing an orthogonal (rectangular) array, using load_gdml_color
<number>

## Slide 34
Adding non-GDML solids to the GDML document
3. Arrays
b. Polar Arrays
View of exported gdml file containing a polar array, using load_gdml_color
Polar arrays are added by selecting the object and executing the polar array command
<number>

## Slide 35
Adding non-GDML solids to the GDML document
3. Arrays
c. Arrays of objects distributed along a path
View of exported gdml file containing a path array, using load_gdml_color
Path arrays are added by selecting the object, a curve (path) in 3D and executing the path array command
<number>

## Slide 36
Adding non-GDML solids to the GDML document
3. Arrays
e. Arrays of arrays
View of the exported gdml file containing an orthogonal array of a polar array, using load_gdml_color
Any object that can be exported to GDML by the Workbench can serve as the base of an array. Below shows an orthogonal array of a polar array of a Cut of two solids in FreeCAD.
<number>

## Slide 37
Adding non-GDML solids to the GDML document
Any solid can be exported to a gdml file by meshing it then tessellating the mesh
Example:
View of exported gdml file containing a tessellation, using load_gdml_color
Part Workbench can create a solid by sweeping one sketch to another along a path. GDML Workbench currently cannot export a sweep.
Can convert the sweep shape to a tessellated solid using the Part to Mesh command
<number>

## Slide 38: Opticals Support
With GDML workbench activated, open new file
  Creates GDML file structure
    Matrix
    Surfaces
Import matrix.xml file see example freecad/gdml/Resources/matrix.xml
  Matrix is a number of FreeCAD spreadsheets within the Opticals/Matrix Group
Import optical.xml file see example freecad/gdml/Resources/optical.xml
  Definition of a number of surfaces
Icons/Commands
  Set Skin Surface
  Set Border Surface
<number>

## Slide 39: Other Information
Information on the GDML workbench can be found on Keith’s github page: https://github.com/KeithSloan/GDML
Installation - see README in github
  Gmsh shared library needs to be installed in FreeCAD Resources/lib see README
Use instructions and example files are on the wiki page https://github.com/KeithSloan/GDML/wiki
<number>

## Slide 40: Future
Command line scripts
User defined materials in FreeCAD User-defined materials can be imported into the Workbench, but not defined in it
GUI creation of more solids Although all solids defined under GDML are implemented, the lesser common ones do not have corresponding commands/icons to create them in the GDML Workbench. Currently can import all solids, so one without an icon can be imported into a document from a gdml file
Check for overlapping solids in FreeCAD itself
Closer match between exported and imported GDML files
Need Help! Both Keith and I are in our early 70’s and probably cannot continue to maintain the project far into the future. Would like to get younger people who are competent in python involved in the project with a view to eventually taking over the maintenance. We would be willing to mentor anyone who is interested!
<number>

## Slide 41: Thanks
Jim Austin (icon designs)
Emmanuel Delage, Wouter Deconnick, Louis Helary
Damian Lambert, Paulo Dondero, Ami Hashemi
John Watts, Frederico-Carminati
Hilden Timo, Atanu Quant, Masaki Morita
Large number from the FreeCAD community Please see github README
See also GitHub Contributors
<number>

## Slide 42
Extra Slides
<number>

## Slide 43: Correspondence between FreeCAD document structure and GDML document structure
<volume name="DaughterVol_1">
...
<volume name="DaughterVol_2">
...
<volume name="MotherVolume">
<materialref ref="G4_A-150_TISSUE"/>
<solidref ref="Box"/>
<physvol name="PV-DaughterVol_1">
<volumeref ref="DaughterVol_1"/>
...(position+rotation)
<physvol name="PV-DaughterVol_2">
<volumeref ref="DaughterVol_2"/>
...(position+rotation)
</volume>
<volume name="V-GDMLElTube001">
...
<volume name="V-GDMLSphere001">
...
<assembly name="Assembly">
<physvol name="PV-GDMLElTube001">
<volumeref ref="V-GDMLElTube001"/>
...(position+rotation)
<physvol name="PV-GDMLSphere001">
<volumeref ref="V-GDMLSphere001"/>
...(position+rotation)
</assembly>
<number>

## Slide 44
Adding non-GDML solids to the GDML document
3. Arrays
d. Arrays of objects placed at arbitrary points
View of exported gdml file containing a point array, using load_gdml_color
Point arrays are added by selecting the object, a set of points in 3D and executing the point array command.
Points can be entered in a variety of ways, including using the Points Workbench to read a variety of file formats.
<number>

## Slide 45
Adding non-GDML solids to the GDML document
4. Mirrored object
View of exported gdml file containing a path array, using load_gdml_color
Mirrored objects are added by selecting the object, a reflection plane and executing the mirror command.
<number>

## Slide 46: GDML Workbench History
  CAD-GDML - Meeting at SLAC Sept 2011
    C++ Workbench started by Emmanuel Delage
  Initial Workbench FreeCAD_Python_GDML
      Geant4 python library which at the time was still under development
      Now GitHub retired / archived
  GDML workbench – Created and maintained by Keith Sloan https://github.com/KeithSloan/GDML
      Different approach
      GDML Solids implemented as FreeCAD FeaturePython Objects
      Recent enhancements - Thanks to Munther Hindi (joined the project November 2021)
        Arrays, Mirrors
        Extruded and Revolved Sketches
<number>